## Slide 1: CS3220 Processor Design
Prof. Hyesoon Kim

## Slide 2: CS3220
Instructor: Prof. Hyesoon Kim
Class time: M/W 2:00-3:15 pm
Most of the time, only Wed is a live lecture.
For some weeks, there are lab sessions which we split into two sessions.
Lab days: in-class assignments are given and need to submit them by the end of 2nd lab days.
Earlier lectures require to watch recorded videos.
Classroom: Virtual
Resource: Canvas, Piazza,

## Slide 3: FPGA vs. ASIC
http://anysilicon.com/wp-content/uploads/2016/01/FPGA-vs-ASIC.jpg
NRE: Non-recurring engineering costs
NRE: recurring engineering cost
FPGA: Field Programmable Gate Arrays
Notes: What are the examples? Calculators vs. Processors.

## Slide 4
Interconnect Resources
Logic Block
I/O Cell
CONCEPTUAL FPGA

## Slide 5: FPGA Architectures
How to implement programmable circuits?
High level view:
  Every combination logic is eventually a truth table
  Example: half adder
Input |  | Out
A | B | S
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Input |  | Out
A | B | C
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 6: Look-up-tables (LUTs)
Implement truth table (LUTs) in small memories and program the memory values
  Usually SRAM
A | B | S
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A | B | C
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0
1
1
0
Addr
Output
0
0
0
1
Output
2-input, 1-output LUTs
00
01
10
11
01
10
11
A
B
Addr
A
B
S
C
Address: inputs

## Slide 7: LUTs
Combine two tables: when the outputs are used together
0
1
1
0
S
0
0
0
1
C
0
1
1
0
S
0
0
0
1
C
00
01
10
11
00
01
10
11
00
01
10
11
Addr
Addr
A
B
Addr
A
B

## Slide 8
FPGA designs are program the look-up tables.
Do we write a code to fill out the look up tables?
  Too much work
  Hardware designers write code (from very high level to very low-level)
  Hardware synthesizer will generate the circuitry information
  Sent a series of bits information to the FPGA hardware