## Slide 1: CS3220 Processor Design
Prof. Hyesoon Kim
Slides are based on
Prof. Prvulovic’s CS3220

## Slide 2: Now, programming FPGA
We will use verilog for this course
We will use Xilinix tool chains
Later in the semester, we will use high-level language tool which coverts normal C/C++ program to hardware description language by compilers.

## Slide 3: What is Verilog?
Hardware description language (HDL)
  For designing and modeling hardware
Behavioral or algorithmic level
  Highest level of abstraction. Similar to C
    E.g.) you can use if-else
Other hardware description languages
  VHDL
  SystemC
  High-level languages
Palnitkar’s Verilog HDL

## Slide 4: CAD Flow
Verilog
input a, b;
output [1:0] sum;
assign sum = a+b;
Netlist
g1 “and” n1 n2 n5
g2 “and” n3 n4 n6
g3 “or” n5 n6 n7 …
Mapping
FPGA
ASIC
(Custom ICs)
Compilations and synthesis

## Slide 5: Verilog?
Gate-level
  Modules are implemented in terms of logics and interconnections (gates and wires)
Switch level
  Lowest level of abstraction. Switches, storage nodes
Palnitkar’s Verilog HDL

## Slide 6: Components of a Verilog Module
Palnitkar’s Verilog HDL
Module Name,
Port List, Port Declarations (if ports present)
Parameters (optional)
Declarations of wires, regs and other variables
Data flow statement (assign)
Instantiation of lower level modules
Always and initial blocks,
All behavioral statements go in these blocks
Tasks and functions
endmodule statement

## Slide 7: Modules
module <module name> (<list of ports>);
input <width> <input port name>;
output <width> <output port name>;
<variable declarations>
< statements> // module internals
endmodule
Module statement defines the interface
Each port has to be declared as input or output
width specified as [n-1:0] for a n-bit port
Palnitkar’s Verilog HDL

## Slide 8: Ports : Connect Between Modules
Ports
Verilog keyword
Input : input port
Output: output port
Inout : bidirection port
Module
ports
Notes: Port mismatch is one of the common errors as well

## Slide 9: Simple Verilog Module
  module myxor (c, a, b); // Note: List interface signals
  // Declare interface signals
  output c;
  input a, b;
  // declare internal wires
  wire nota,notb,anotb,bnota;
  // Describe internal circuitry
  not(nota,a); // nota = not a, using not() primitive module
  not(notb,b); // notb = not b
  and(anotb, a, notb); // anotb = a and notb
  and(bnota, b, nota); // bnota=b and nota
  or(c,anotb,bnota);
  endmodule

## Slide 10: Instances
Instantiation
Create real objects
Every module needs to be instantiated inside another module
module myxor;
….
Define myxor
myxor myxor1, myxor2;
Instantiate 2 myxors
Notes: A module provides a template from which you can create actual objects. When a module is invoked, verilog creates a unique object from the template.

## Slide 11: Lexical Conventions
similar to C
comments: // /* */
Operators:
  unary, binary, ternary
    a = ~b, a = b&& c, a = b? c : d;
Operator type
  Arithmetic: * / + - %
  Logical: ! && ||
  Relational > < >= <=
  Equality == != === !==
  Bitwise ! & | ^ ^~ ~^
  Reduction & ~& | ~| ^ ^~ ~^

## Slide 12: Reduction Operators
X = 4’b1010
&X ?
  1 & 0 & 1 & 0  1’b0
|x ?
  1 | 0 | 1 | 0  1’b1
^x
  1^0^1^0  1’b0

## Slide 13: Literals
<size>’<base><number>
All of the following are the same:
  8’b10101111 // binary
  8’hAF // hex
  {4’hA, 4’b1111} // concatenation
  {4’hA, {4{1’b1}}} // repeat the same signal
Verilog provides the following 4 values
  0: logic zero or false condition
  1: logic one, or true condition
  x: unknown/undefined logic value, only for physical data types
  z: high-impedance/floating state. Only for physical data types
Notes: Data size mismatch never generated an error in the compilation!
One of the common sources of the error

## Slide 14: Registers vs. Wire
Wire
  Represents connection between components
  Its value is determined by the value of its drivers
  Its default value is z (high-impedance)
Reg
  Retains its value until next assignment
  Its default value is x
Reg does not mean register in the hardware. Just a variable type.
https://cs.uwaterloo.ca/~oardakan/files/Verilog-Intro.pdf

## Slide 15: Conditional Operator
usage: condition_expr ? true_expr:false_expr
assign addr_bus = drive_enable? addr_out : 36’bz; // MUX behavior
assign out = control? in1: in0
assign out = (A == 3) ? (control ? X :Y) : (control ? m:n);

## Slide 16: Continuous (Dataflow) Assignment
<continous_assignment>
  :: = assign <drive strength>?<delay>?<list_of_assignments>;
  assign out = i1 & i2; // out is a net, i1 and i2 are nets
  assign addr[15:0] = addr_bits[15:0] ^ addr2_bits[15:0];
  // assign for vector nets
  assign {c_out, sum[3:0]} = a[3:0]+b[3:0]+c_in;
  // concatenation , left-hand side is a concatenation of a scalar net and a vector net
  a simple and natural way to represent combinational logic
Implicit continuous assignment
  Only one implicit declaration assignment per wire
Palnitkar’s Verilog HDL
wire out;
assign out = in1 & in2;
 wire out = in1 & in2;

## Slide 17: Always Statement
Always: starts at 0, executes the statements in the always block continuously in a looping fashion
You cannot assign wires while inside an always block
the always block runs once whenever a signal in the sensitivity list changes value
always @(posedge clock)
a = b;
Statements within Always block will be run sequentially
module clock_gen;
reg clock;
initial
clock = 1’b0;
always
#10 clock = ~clock;
initial
#10000 $finish;
endmodule

## Slide 18: General rules for always
Always are used for state-machines, pipeline latches.
always @(*) // always block statements are executed whenever input values are changed
  Combinational logic
always @(clock)
  Put latch events
CS3220 Prof. Milos Prvulovic

## Slide 19: Simulation
Simulation: create all the input signals
  Often means creating more Verilog code and monitors
Testbench: test-only code
Generating inputs
Unit Under Test
Checking Outputs

## Slide 20: Behavioral Simulation
High-level model simulation
Before Synthesis using only HDL
Checking high-level design functional behavior
Without any timing constrains
Fromhttps://www.xilinx.com/support/documentation/sw_manuals/xilinx11/platform_studio/ps_c_sim_behavioral_simulation.htm: