## Slide 1: CS3220 Processor Design
Prof. Hyesoon Kim

## Slide 2: Intermediate wire
module simple_in_n_out ( in_1, in_2,in_3, out_1);
input in_1;
input in_2;
input in_3;
output out_1;
assign out1_ = (in1&in_2) |in3;
endmodule
In_1
In_2
In_3
Out_1

## Slide 3: Intermediate wire
module simple_in_n_out ( in_1, in_2,in_3, out_1);
input in_1;
input in_2;
input in_3;
output out_1;
wire intermediate_sig;
assign intermediate_sig = in1&in_2;
assign out_1 = intermediate_sig & in3;
endmodule
In_1
In_2
In_3
Out_1
intermediate_sig
From: Verilog by example (Readler)

## Slide 4: Testing and Simulation

## Slide 5: Testing myxor
Testing requires another module/another Verilog coding
module my_test;
reg a,b;
wire c;
localparam period=20;
myxor myxor1(.c(c), .a(a), .b(b));
initial
begin
a = 0;
b = 0;
#period;
a = 0;
b = 1;
#period;
end

## Slide 6: Conditional Statements
if and else are used for conditional statements
  if (<expression>) true_statement;
  if (<expression> true_statement; else false_statement;
  if (<expression>) true_statement1;
  else if (<expression>) true_statement2;
  else default_statement;
Case statement
  case (expression)
    alternative1: statement1;
    alterantive2: statement2;
    alternative3: statement3;
    …
    default: default_statement;
    endcase

## Slide 7: Lab DAY #2 Contents

## Slide 8: Bus Signals
module bus_sigs ( in_1, in_2,in_3, out_1);
input [3:0] in_1;
input [3:0] in_2;
input in_3;
output [3:0] out_1;
wire [3:0] in_3_bus;
assign in_3_bus = {4{in_3}};
assign out_1 = (in_1 & in_2 ) | ~in_3_bus;
endmodule
In_3 is replicated 4 times
From: Verilog by example (Readler)

## Slide 9: Bus Breakout
Concatenation
BUS = {out_1, out_2};
BUS_2 = {BUS[3:0], out[2:0]};

## Slide 10: MUX examples
wire A, B, C, D;
reg out;
wire out1, out2, out3, out4;
wire[1:0] sel;
assign out1 = A & ! sel[1] & !sel[0];
assign out2 = B & ! sel[1] & sel[0];
assign out3 = C & sel[1] & !sel[0];
assign out4 = D & sel[1] & sel[0];
assign out = out1 | out 2| out3 | out 4;

## Slide 11: Verilog description of MUX
wire A, B, C, D;
reg out;
wire [1:0] sel;
assign out = (sel==2’b00) ? A : 1’bz,
out = (sel==2’b01) ? B : 1’bz,
out = (sel==2’b10) ? C : 1’bz,
out = (sel==2’b11) ? D : 1’b z;

## Slide 12: Verilog description of MUX
wire A, B, C, D;
reg out;
wire [1:0] sel;
always @(A or B or C or D or sel)
case (sel)
2’b00: out = A;
2’b01: out = B;
2’b10: out = C;
2’b11: out = D;
default: out = 1’bz;

## Slide 13: Vectors vs. Arrays
Vectors
  To define multiple width wires or registers
  Definition:
    Wire/reg[msb_index: lsb_index] <data_id>;
Arrays
  It is possible to have reg, integer and time arrays
  Definition:
    <data_type> <var_name> [start_idx : end_idx]
https://cs.uwaterloo.ca/~oardakan/files/Verilog-Intro.pdf

## Slide 14: n-bit signals
Multi-bit signals
2-to-1 multiplexer with 8-bit operands
module mux_2_to_1 (a,b, out, outbar, sel);
input[7:0] a,b;
input sel;
output[7:0] out, outbar;
reg[7:0] out;
always @(a or b or sel)
begin
if (sel) out = a;
else out = b;
end
assign outbar ~=out;
endmodule
a
b
out
outbar
sel
8
8
8
8
http://web.mit.edu/6.111/www/f2007/handouts/L04.pdf

## Slide 15: State Machines

## Slide 16: Sequential Circuits
Combinational Logic
in
out
state
Output of sequential circuits depends not only the current state but also the history of the previous state

## Slide 17: Synchronous Sequential Circuits
Synchronized to a clock signal
: finite-state machine (FSMs)
Combinational Logic
in
out
state
clk
D Q

## Slide 18: Simple D-flop
From Verilog by example book (Readler)

## Slide 19: D-flop with reset
From Verilog by example book (Readler)

## Slide 20: Blocking vs. Nonblocking Assignment
Blocking assignments: executed in the order they are specified in a sequential block
Nonblocking assignments: (<=) assignments allow scheduling without blocking execution of the statements that follow in a sequential block
reg a, b;
initial
begin
a = state1;
b = state2;
end
reg a, b;
initial
begin
a <= state1;
b <= state2;
end

## Slide 21: State Machine
From Verilog by example book (Readler)

## Slide 22: General rules for always
always @(*)
  Combinational logic
always @(clock)
  Put latch events
Inside always : please put only logics.
  Don’t declare wire,regs
  Don’t instantiate a module inside always block.
CS3220 Prof. Milos Prvulovic

## Slide 23: Note:
Don’t put
  “output<= “ in multiple always statements
Why not?
  Not synthesizable: Compiler can or cannot generate combinational logic circuits from verilog code
always @(posedge clk) begin
if (cond1)
count <= ….
end
always @(posedge clk)
begin
If (cond2)
count <= …
end
+
always @(posedge clk) begin
if (cond1)
count <= ….
else if (cond2)
count <= …
end
count should be a ”reg” type
count cannot be “wire” type

## Slide 24: Memory

## Slide 25: Memories in Verilog
reg [15:0] mem[0:1023].  reg [15:0] mem[1023:0] are the same.
  Data width
Now, let’s just think memory is a group of registers.
This is not really true but let’s just do that for now.
Total size of memory = 16b x 2^1024  2KB
Size of memory

## Slide 26: How to initialize Memory Values?
This is an option to use for behavior simulation
reg [15:0] dmem[0:1023]
initial begin
$readmemh("ex1.mem", dmem);
end

## Slide 27: Synchronous read vs. Asynchronous read
Synchronous (clocked) read
  always @(posedge clock) begin
  mdr <= dmem[mar]; // Read memory
  end
Asynchronous read
  assign read_data = dmem[mar];

## Slide 28: Defining Memory in FPGA
(1) Infer the memory directly via the Verilog code
(2) Build the memory using the vendor’s primitive RAM structures
(3) Design the memory using the FPGA vendor’s specialized tools
From:Verilog by example Blaine C. Readler

## Slide 29: Inference vs. Instantiation
Verilog can use “inference” or “instantiation” memory
Inference in synthesis: portable coding style, automatic timing-driven synthesis,
Instantiation: efficient use of the FPGA based on the specific technology, supports all kinds of RAM
We use “inference” method
From:http://www.ee.hacettepe.edu.tr/~alkar/ELE432/ECE432_memory_5.pdf