## Slide 1: CS3220 Processor Design
Prof. Hyesoon Kim

## Slide 2: Fixed Point FP

## Slide 3: Fixed Point Operation
Use integer operators to calculate floating point operations
Fixed point integer
12.23 1223
+20.41 + 2041
-------------- --------------
32.64 3264
12.23 1223
x 20.41 x 2041
-------------- --------------
249.61 2496143
a 1.15.16 fixed point number: one bit sign, 15-bit integer, 16-bit fraction. 1+15+16 = 32
Fixed fraction

## Slide 4: Fixed Point Operation Types in real hardware
E.g) Nintendo DS device
v16 = 1.3.12 fixed point number (used for 3D)
t16 = 1.11.4 fixed point number
f32 = 1.19.12 fixed point number (used for matrices)
v10 = 1.0.9 fixed point number (whoops! 10 bits don't fit into a normal integer? but 3 v10 numbers fit into a 32 bit integer, so this format is used for normals in 3D (it's also ok for normals to be between -1 and 1, so this is why these fixed point numbers have a long fraction but no integer part!)
0.8.8 fixed point number: this format is used for the scaling of the extended rotation backgrounds and doesn't have a typedef in the NDSlib.

## Slide 5: Floating point
From: http://www.pitt.edu/~juy9/142/slides/L5-Multiplication.ppt

## Slide 6: IEEE Floating Point
IEEE Standard 754
  Established in 1985 as uniform standard for floating point arithmetic
    Before that, many idiosyncratic formats
  Supported by all major CPUs
Driven by Numerical Concerns
  Nice standards for rounding, overflow, underflow
  Hard to make go fast
    Numerical analysts predominated over hardware types in defining standard
From: www.cs.cmu.edu/afs/cs/academic/class/15213-s01/lectures/class10.ppt

## Slide 7: Fractional Binary Numbers
Representation
  Bits to right of “binary point” represent fractional powers of 2
  Represents rational number:
bi
bi–1
b2
b1
b0
b–1
b–2
b–3
b–j
• • •
• • •
.
1
2
4
2i–1
2i
• • •
• • •
1/2
1/4
1/8
2–j
From: www.cs.cmu.edu/afs/cs/academic/class/15213-s01/lectures/class10.ppt

## Slide 8: Fractional Binary Number Examples
Value Representation
  5-3/4 101.112
  2-7/8 10.1112
  63/64 0.1111112
Observation
  Divide by 2 by shifting right
  Numbers of form 0.111111…2 just below 1.0
    Use notation 1.0 – 
Limitation
  Can only exactly represent numbers of the form x/2k
  Other numbers have repeating bit representations
Value Representation
  1/3 0.0101010101[01]…2
  1/5 0.001100110011[0011]…2
  1/10 0.0001100110011[0011]…2
From: www.cs.cmu.edu/afs/cs/academic/class/15213-s01/lectures/class10.ppt

## Slide 9: Floating Point Representation
Numerical Form
  –1s M 2E
    Sign bit s determines whether number is negative or positive
    Significand M normally a fractional value in range [1.0,2.0).
    Exponent E weights value by power of two
Encoding
  MSB is sign bit
  exp field encodes E
  frac field encodes M
Sizes
  Single precision: 8 exp bits, 23 frac bits
    32 bits total
  Double precision: 11 exp bits, 52 frac bits
    64 bits total
s
exp
frac
From: www.cs.cmu.edu/afs/cs/academic/class/15213-s01/lectures/class10.ppt
Mantissa = Fraction

## Slide 10: “Normalized” Numeric Values
Condition
  exp  000…0 and exp  111…1
Exponent coded as biased value
  E = Exp – Bias
    Exp : unsigned value denoted by exp
    Bias : Bias value
      Single precision: 127 (Exp: 1…254, E: -126…127)
      Double precision: 1023 (Exp: 1…2046, E: -1022…1023)
      in general: Bias = 2m-1 - 1, where m is the number of exponent bits
Significand coded with implied leading 1
  m = 1.xxx…x2
    xxx…x: bits of frac
    Minimum when 000…0 (M = 1.0)
    Maximum when 111…1 (M = 2.0 – )
    Get extra leading bit for “free”
From: www.cs.cmu.edu/afs/cs/academic/class/15213-s01/lectures/class10.ppt

## Slide 11: Normalized Encoding Example
Value
  Float F = 15213.0;
  1521310 = 111011011011012 = 1.11011011011012 X 213
Significand
  M = 1.11011011011012
  frac = 110110110110100000000002
Exponent
  E = 13
  Bias = 127
  Exp = 140 = 100011002
Floating Point Representation:
Hex: 4 6 6 D B 4 0 0 Binary: 0100 0110 0110 1101 1011 0100 0000 0000
140: 100 0110 0
15213: 1110 1101 1011 01
From: www.cs.cmu.edu/afs/cs/academic/class/15213-s01/lectures/class10.ppt

## Slide 12: Denormalized Values
Condition
  exp = 000…0
Value
  Exponent value E = –Bias + 1
  Significand value m = 0.xxx…x2
    xxx…x: bits of frac
Cases
  exp = 000…0, frac = 000…0
    Represents value 0
    Note that have distinct values +0 and –0
  exp = 000…0, frac  000…0
    Numbers very close to 0.0
    Lose precision as get smaller
    “Gradual underflow”
From: www.cs.cmu.edu/afs/cs/academic/class/15213-s01/lectures/class10.ppt

## Slide 13: Special Values
Condition
  exp = 111…1
Cases
  exp = 111…1, frac = 000…0
    Represents value(infinity)
    Operation that overflows
    Both positive and negative
    E.g., 1.0/0.0 = 1.0/0.0 = +, 1.0/0.0 = 
  exp = 111…1, frac  000…0
    Not-a-Number (NaN)
    Represents case when no numeric value can be determined
    E.g., sqrt(–1), 
From: www.cs.cmu.edu/afs/cs/academic/class/15213-s01/lectures/class10.ppt

## Slide 14: Summary of Floating Point Real Number Encodings
NaN
NaN
+

0
+Denorm
+Normalized
-Denorm
-Normalized
+0
From: www.cs.cmu.edu/afs/cs/academic/class/15213-s01/lectures/class10.ppt

## Slide 15: Tiny floating point example
8-bit Floating Point Representation
  the sign bit is in the most significant bit.
  the next four bits are the exponent, with a bias of 7.
  the last three bits are the frac
Same General Form as IEEE Format
  normalized, denormalized
  representation of 0, NaN, infinity
s
exp
frac
0
2
3
6
7
From: www.cs.cmu.edu/afs/cs/academic/class/15213-s01/lectures/class10.ppt

## Slide 16: Values related to the exponent
Exp exp E 2E
0 0000 -6 1/64 (denorms)
1 0001 -6 1/64
2 0010 -5 1/32
3 0011 -4 1/16
4 0100 -3 1/8
5 0101 -2 1/4
6 0110 -1 1/2
7 0111 0 1
8 1000 +1 2
9 1001 +2 4
10 1010 +3 8
11 1011 +4 16
12 1100 +5 32
13 1101 +6 64
14 1110 +7 128
15 1111 n/a (inf, NaN)
From: www.cs.cmu.edu/afs/cs/academic/class/15213-s01/lectures/class10.ppt

## Slide 17: Dynamic Range
s exp frac E Value
0 0000 000 -6 0
0 0000 001 -6 1/8*1/64 = 1/512
0 0000 010 -6 2/8*1/64 = 2/512
…
0 0000 110 -6 6/8*1/64 = 6/512
0 0000 111 -6 7/8*1/64 = 7/512
0 0001 000 -6 8/8*1/64 = 8/512
0 0001 001 -6 9/8*1/64 = 9/512
…
0 0110 110 -1 14/8*1/2 = 14/16
0 0110 111 -1 15/8*1/2 = 15/16
0 0111 000 0 8/8*1 = 1
0 0111 001 0 9/8*1 = 9/8
0 0111 010 0 10/8*1 = 10/8
…
0 1110 110 7 14/8*128 = 224
0 1110 111 7 15/8*128 = 240
0 1111 000 n/a inf
closest to zero
largest denorm
smallest norm
closest to 1 below
closest to 1 above
largest norm
Denormalized
numbers
Normalized
numbers
From: www.cs.cmu.edu/afs/cs/academic/class/15213-s01/lectures/class10.ppt

## Slide 18: Interesting Numbers
Description exp frac Numeric Value
Zero 00…00 00…00 0.0
Smallest Pos. Denorm. 00…00 00…01 2– {23,52} X 2– {126,1022}
  Single  1.4 X 10–45
  Double  4.9 X 10–324
Largest Denormalized 00…00 11…11 (1.0 – ) X 2– {126,1022}
  Single  1.18 X 10–38
  Double  2.2 X 10–308
Smallest Pos. Normalized 00…01 00…00 1.0 X 2– {126,1022}
  Just larger than largest denormalized
One 01…11 00…00 1.0
Largest Normalized 11…10 11…11 (2.0 – ) X 2{127,1023}
  Single  3.4 X 1038
  Double  1.8 X 10308
From: www.cs.cmu.edu/afs/cs/academic/class/15213-s01/lectures/class10.ppt

## Slide 19: Special Properties of Encoding
FP Zero Same as Integer Zero
  All bits = 0
Can (Almost) Use Unsigned Integer Comparison
  Must first compare sign bits
  Must consider -0 = 0
  NaNs problematic
    Will be greater than any other values
    What should comparison yield?
  Otherwise OK
    Denorm vs. normalized
    Normalized vs. infinity
From: www.cs.cmu.edu/afs/cs/academic/class/15213-s01/lectures/class10.ppt

## Slide 20: FP Multiplication
Operands
  (–1)s1 M1 2E1
  (–1)s2 M2 2E2
Exact Result
  (–1)s M 2E
  Sign s: s1 ^ s2
  Significand M: M1 * M2
  Exponent E: E1 + E2
Fixing
  If M ≥ 2, shift M right, increment E
  If E out of range, overflow
  Round M to fit frac precision
Implementation
  Biggest chore is multiplying significands
From: www.cs.cmu.edu/afs/cs/academic/class/15213-s01/lectures/class10.ppt

## Slide 21: FP Addition
Operands
  (–1)s1 M1 2E1
  (–1)s2 M2 2E2
  Assume E1 > E2
Exact Result
  (–1)s M 2E
  Sign s, significand M:
    Result of signed align & add
  Exponent E: E1
Fixing
  If M ≥ 2, shift M right, increment E
  if M < 1, shift M left k positions, decrement E by k
  Overflow if E out of range
  Round M to fit frac precision
  (–1)s1 m1
  (–1)s2 m2
E1–E2
+
  (–1)s m
From: www.cs.cmu.edu/afs/cs/academic/class/15213-s01/lectures/class10.ppt

## Slide 22: New FP formats with Machine learning

## Slide 23: Different Floating Points
From:https://en.wikipedia.org/wiki/Bfloat16_floating-point_format

## Slide 24: BF16
From:https://en.wikipedia.org/wiki/Bfloat16_floating-point_format

## Slide 25: Pros of Low-precision computing
Can fit more numbers (and therefore more training examples, activations, etc.) in memory
Can store more numbers (and therefore larger models) in the cache
Can transmit more numbers per second
Can compute faster by extracting more parallelism in a fixed-width SIMD register
Uses less energy Cons of low-precision computing.
Limits the range of numbers we can represent (the range between the overflow and underflow thresholds)
Need specialized support from the hardware
Introduces quantization error when we store a full-precision number in a low-precision representation
https://www.cs.cornell.edu/courses/cs4787/2019sp/notes/lecture23.pdf