## Slide 1: CS3220 Processor Design
Prof. Hyesoon Kim

## Slide 2: Pipelining the pipeline
Let’s remember the single-bus datapath
We’ll divide it into 5 stages
  Fetch
  Decode/RF Access
  Address Generation/Execute
  Memory
  Store Result
Conservative handling of data and control dependences
  Stall on branch
  Stall on flow (data) dependence

## Slide 4: An Example LC-3b Pipeline

## Slide 5: 5 stage pipeline
IF: Instruction fetch
ID/RR: instruction decoding & Register reading
EX: Execution
MEM: memory accesses
WB: Register writeback
IF
ID/RR
EX
MEM
WB

## Slide 6: Example: Execution of Four Independent ADDs
Multi-cycle: 5 cycles per instruction
Pipelined: 5 cycles per 5 instructions (steady state)
Time
Time
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W

## Slide 7: Pipeline Hazard
Control-flow hazard
  How to handle branch instructions
Data-flow hazard
  Data dependency
Designing how to handle pipeline hazard is the key component of this assignment

## Slide 8: Data Dependence Types
Flow dependence
      r3  r1 op r2 Read-after-Write
      r5  r3 op r4 (RAW)
Anti dependence
      r3  r1 op r2 Write-after-Read
      r1  r4 op r5 (WAR)
Output-dependence
      r3  r1 op r2 Write-after-Write
      r5  r3 op r4 (WAW)
      r3  r6 op r7

## Slide 9: Dependency logic
Method 1: Scoreboard
  At Decode stage, set busy bit for the destination register and at the write back stage, set clear the busy bit (multi-count busy bits will be required instead of 1-bit)
  Caution! : We can write and read the same register by the same instruction
Method 2: check destination register ids
  Forward destination ids from other pipeline stages
  Be careful to check when destination registers are indeed used. Not all instructions have source registers

## Slide 10: FAQ
Can we use data forwarding?
  We don’t recommend for this assignment.
  Data forwarding will change the performance behavior significantly

## Slide 11: Pipeline Latches

## Slide 12: An Example LC-3b Pipeline

## Slide 13: Pipeline Latch
Latch vs. combination logic
  Latch: Holds a value. Out value will be available after a new clock.
Combinational Logic
CLK
<in>
<out>
CLK
1
1
in
out
2
3
4
5
6
2
5
6
This example is based on positive edge clock

## Slide 14: How to make a pipeline stall?
Option #1: Send the data out back to data in
Option #2: Have an ” enable” signal and set “0” into a write enable signal
Latch
MUX
Data in
Data out
select
clk
Latch
clk
Data in
Enable

## Slide 15: How to flush a pipeline
Latch
MUX
Data in
Data out
select
clk
Valid

## Slide 16: Front-end Pipeline
PC (register) : holds a value to indicate where to fetch
W/o branch, next_pc = current_pc + instruction_size
I-cache
PC
instruction
PC
…
Front Latch
CLK
CLK
Next PC compute logic

## Slide 17: How to handle branch?
I-cache
PC
CLK
CLK
Next PC compute logic
Inst
Decode logic
Branch?
br cond target 0x800
add r1, r2,r3 0x804
target sub r2,r3,r4 0x900
0x800
0x800
br
br
0x804
0x804
add
V
Flush
1
Cycle 1
Cycle 2
0

## Slide 18: Handling Branches
FE
ID
EX
MEM
WB
br
0x800
br
0x804
br
br
br
0x804
0x900
0x904
PC (latch)
add
add
sub
add
0x908
1
cycle
2
3
4
5
6
mul
sub
sub
add
FE_stage
br cond target 0x800
add r1, r2,r3 0x804
target sub r2,r3,r4 0x900

## Slide 19: Handling Branches- Alt
FE
ID
EX
MEM
WB
br
0x800
br
0x804
br
br
br
0x804
0x904
0x908
PC (latch)
add
sub
sub
add
0x90b
1
cycle
2
3
4
5
6
div
mul
mul
add
mul
sub
sub
FE_stage
br cond target 0x800
add r1, r2,r3 0x804
target sub r2,r3,r4 0x900

## Slide 20: Which option to choose?
We recommend to have two pipeline bubbles.
  But how many bubbles in the pipeline is dependent on your design decision.
1 pipeline bubbles looks so better, why are you suggesting 2 pipeline bubbles?
  It will increase critical path.
  It will be a design trade-off between clock frequency vs. pipeline bubbles.

## Slide 21: Handling Branches: V
FE
ID
EX
MEM
WB
br
0x800
br
0x804
br
br
br
0x804
0x900
0x904
PC (latch)
add
add
sub
add
0x908
1
cycle
2
3
4
5
6
mul
sub
sub
add
FE_stage
br cond target 0x800
add r1, r2,r3 0x804
target sub r2,r3,r4 0x900

## Slide 22: Handling Branches: II
FE
ID
EX
MEM
WB
br
0x800
br
0x804
br
br
br
0x804
0x804
0x900
PC (latch)
add
add
add
sub
0x904
1
cycle
2
3
4
5
6
add
sub
FE_stage
br cond target 0x800
add r1, r2,r3 0x804
target sub r2,r3,r4 0x900

## Slide 23: Assignment #1
Draw a pipeline (5 stages)
Draw a dependence check logic (or scoreboard)
Show how you stall the pipeline (insert pipeline bubbles or put invalid in the latches)
Show all backward signals (signals from the later pipeline stages to the earlier pipeline stages)
Submit a video of explaining the pipeline. The detailed descriptions are in Canvas.