## Slide 1: CS3220 Processor Design
Prof. Hyesoon Kim

## Slide 2: 5 stage pipeline
IF: Instruction fetch
ID/RR: instruction decoding & Register reading
EX: Execution/Address generation
MEM: memory accesses
WB: Register writeback
IF
ID/RR
EX
MEM
WB

## Slide 3: Assignment #1
Design a 5-stage pipeline (just draw a diagram) and explain your design
  You can use any software to draw the diagram or hand-drawing is fine.
All control signals need to be included (indicate the number of bits)
Clear differentiation between combinational logic vs. latches/flip-flop
No data forwarding
  Register can be written in the first half cycle and can be read in the second half cycle
No branch prediction: Stall at a branch
What to submit? A video of explaining your pipeline design.

## Slide 4: Processor Design
Processor needs an ISA

## Slide 5: Project ISA
We need to design an ISA
ISA requirement
  Easy to decode (you have to write this in verilog)
  Easy to write assembler
  Easy to write applications (you will do this too!)
Similar tradeoff involved in designing real CPUs
  Plus backward compatibility
  But CS3220, we don’t want backward compatibility!

## Slide 6: ISA decisions
CISC vs. RISC?
  Definitely RISC (much easier to design)
Fixed-size or variable size ?
  Definitely fixed (fetch and decode design is much easier)
How many things can be read or written ?
  Each register read (>1) complicates register file
  Each register write (>1) complicates register file a lot!
  Each memory read or write (>1) creates lots of problems (memory ports, pipeline stages, hazards)

## Slide 7: Which instructions? Memory!
How will we access memory?
  Do we use only LD/ST or do we allow memory operations in other kinds of instructions?
Only LD/ST is far simple to implement because
  Mem operations in ADD, SUB, etc. require many ”flavors” for each instruction (hard to decode)
    And we need to describe the entire decoding logic in verilog
  Don’t want multiple memory accesses per inst!
    Even one memory stage in the pipeline is complex enough
OK, we will have LW, SW!

## Slide 8: Which instructions? ALU!
Let’s have some arithmetic
  ADD, SUB, what else?
How about some logic?
  Option 1: AND, OR, NOT, XOR, etc.
  Option 2: Let’s just have one! Which one? NAND!
Can “fake” others using NAND, e.g. “NOT A” is “A NAND A”
  Let’s use Option 1 but not go overboard
    Easier to write assembler, easier to decode
    But leave room (unused opcodes) for more
Comparisons? It depends…
  Option 1: Conditional branches do comparisons
  Option 2: Comparison instructions, one cond. branch
  Option 3: Mix of the two

## Slide 9: Branches…
Conditional branches
  PC relative, need decent-sized offset operand
  Hard to write if-then-else and loops if branch only goes e.g. 3 instructions forward or back
How will we call procedures?
  Option 1: Special branch that saves return address
  Option 2: Save RA in SW, use normal branch
How will we return from procedures?
  Option 1: Specialized “RET”
  Option 2: Jump-to-address-in-register (JR)
Let’s have only two call/jump/return insts for now!
  Both are similar to JAL instruction from CS 2200
  JALI Rdst,Imm and JAL Rdst,Rsrc

## Slide 10: Conditional branches?
Typical conditional branches
  BEQ R1,R2,Label ; Go to Label if R1==R2
  Can also have BLT, BLE, BNE, BGT, BGE
  Need to encode two registers in the instruction
  BEQZ R1, Label ; Go to Label if R1==0
  Can also have BNEZ, BLEZ, etc.
  Need to encode only one register in the instruction (so we can have a 6-bit offset)
Could have implicit operand, e.g. always R1
  BEQZ Label ; If R1==0 go to Label
  Bad: R1 won’t be very useful for anything else

## Slide 11: How many registers?
Need at least 2 to do ALU operations
Plus one to be a stack pointer
Plus one to save return address
  Unless we want to save it directly to memory
Nice to have a few extra
  One for return value (to avoid saving it to stack)
  Some to pass parameters? Need at least 2 (more is even better)
Need at least one for system use
  We’ll work on this in the last two projects
OK, this is already 8 or more, so let’s have 16
  When writing code in assembler, we’ll see that more is better 

## Slide 12: Size of instruction word?
Bits in instruction word? Hmm, let’s see
  Need room for opcode
    How many types of instructions do we have?
    Can have a secondary opcode for some (e.g. for ADD,SUB, etc.)
  Need room for register operands
    Do we want 1, 2, or 3 or those? 3!
    This will use 12 bits in the instruction word
  Need room for immediate operands
    The more the better, but too few will be a problem
Let’s have 32-bit instruction word
  8 not really an option (not enough room)
  16 is very tight (with 16 regs, only 4 bits left for opcode)
  So let’s do 32 (allows large offsets, more opcodes, etc.)

## Slide 13: Register size?
How about 8?
  Will need multi-word values often (e.g. loop counters)
  PC must be larger than this, procedure calls get tricky
Can we do with 16?
  Most loops and programs will be OK
  Immediate operand can load entire constant (nice)
  Can display entire word on HEX display 
But it makes sense to have 32-bit registers
  Same as instruction word
  Almost never have to worry about overflows and such

## Slide 14: Memory addressing?
Byte-addressed or word-addressed?
Word-addressed is simpler
  Only need LD/ST instruction, vs. LW/SW, LB/SB, etc.
  Don’t have to worry about alignment
But
  Hard to switch apps to byte-addressed later
  Can’t use e.g. 16-bit memory locations
  We can achieve most of the HW simplicity if we require word-alignment
So we’ll have byte-addressed aligned LW/SW only
  Can drop alignment limitations later if we want to
  But can add LB/SB, LH/SH later if we want to

## Slide 15: Other options
Predicated instructions
Vector instructions

## Slide 16: ISA definition
How many bits for the opcode?
For insts w/ 3 reg operands, 12 bits already used
  Great, leaves 20 bits for opcode! But…
For insts w/ 2 reg and 1 imm operand
  E.g. LW R1,-4(R2), ADDI R1,R2,64, BNE R1,R2,Label
  Imm and opcode must fit in 24 bits (8 used for regno)
Let’s have a 16-bit immediate and 6-bit opcode
  Will make register number decoding a bit easier 
  Few “reach” issues in branches and LW/SW 
  Fairly large constants in ADDI, SUBI, ANDI, etc. 
  We have 64 opcodes
    Sounds like a lot, but it is actually too few:
      LW, SW, ADD, SUB, AND, OR, NAND, etc.
    Will need a trick called “secondary opcode” to for >64 instructions

## Slide 17: Instruction Format Thus Far
wire [5:0] op1; // Primary opcode
wire [3:0] rd,rs,rt; // Register operands
wire [15:0] imm; // 16-bit immediate operand
assign {op1,rd,rs,rt,imm}=iword;
assign rd = iword[8:6];
assign imm = iword[23:8]; // overlap with rd!!!
Source register numbers are always rs and rt
For 3-register instructions, rd is destination
  ADD Rd,Rs,Rt
What about ADDI Reg,Reg,Immed?
  Only one source register (so it should be Rs)
  But Rd CANNOT be the destination (Why?)
  ADDI Rt,Rs,Imm

## Slide 18: Instruction Format Thus Far
wire [5:0] op1; // Primary opcode
wire [3:0] rd,rs,rt; // Register operands
wire [15:0] imm; // 16-bit immediate operand
assign {op1,rd,rs,rt,imm}=iword;
assign rd = iword[8:6];
assign imm = iword[23:8]; // overlap with rd!!! Only 64 opcodes
  LW, SW : 2+
    (and leave room for LHS, LHU, LBS, SBU, SH, SB): 6
  ADD, SUB, AND, OR, XOR, NAND, NOR, NXOR,EQ, NE, LE, LT, GT, GE, LE 15+
  (and leave room for MUL, DIV, SXT,SHL, SHR, …) 15
  BEQ, BNE, BLT, BGT, BGE, BLE 6+
  BEQZ, BNEZ, BLTZ, BGTZ, BLEZ, BGEZ
  JAL 1
  Will need at least 4-5 system insts5
  This is already 24, might need to add at least 26
    Getting kind of tight…

## Slide 19: Instruction Format Options
Opcode:[31:26] |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Opcode:[31:26] |  |  | Imm [23:8] |  |  |  |  |  |  | 
31
16
15
0
{opcode}
{opcode, imm}
{opcode, rd,rs,rt}
{opcode, rs, rt, imm}
Opcode:[31:26] |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | Rd[11:9] |  |  | Rs[8:4] |  |  |  | Rt[3:0] |  |  | 
Opcode:[31:26] |  |  | Imm [23:8] | 
 |  |  | Rs[8:4] | Rt[3:0]

## Slide 20: Final Instruction Format
{opcode, rs, rt, imm}
{opcode, OP2, rd, rs, rt}
Note: Opcode should be 6’b00000
Opcode:[31:26] |  |  | Imm [23:8] | 
 |  |  | Rs[7:4] | Rt[3:0]
Opcode:[31:26] |  |  |  |  | OP2[25:18] |  |  |  | 
 |  |  |  | Rd[11:8] |  | Rs[7:4] | Rt[3:0] |  | 

## Slide 21: Primary/Secondary Opcode
Have a smaller primary opcode (6 bits)
  Instructions without an imm operand have 14 “free” bits
    ADD Rd,Rs,Rt uses 18 bits for primary opcode and regs
  Instructions with an imm but only two regs have 4 free bits
    LW Rd,Imm(Rs) does not use the Rt field
      Also ADDI Rd,Rs,Imm, SUBI, etc.
    SW Rt,Imm(Rs) does not use the Rd field
      Also BEQ Rs,Rt,Imm, etc.
Idea: Use these extra bits for a secondary opcode
  Uses only one primary opcode for a family of ALU instructions
  Secondary opcode => the actual operation
Primary opcode of 000000 now means “3-reg ALU inst”
  Imm field unused => Secondary opcode can be up to 14 bits

## Slide 22: Assign Primary Opcodes
Does it matter which insts get which opcode?
  E.g. ALU Rd,Rs,Rt 000000, ALU Rd,Rs,Imm is 000001, etc.?
Make the decoding easy!
  After we read the primary opcode, need to look at secondary opcode to finish decoding
  Let some opcode bits tell us where the op2 is!
Assigning opcode numbers as a list is messy
  So we use an opcode chart

## Slide 23: Opcode Chart
category |  | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
EXT | 000 | EXT |  |  |  |  |  |  | 
BR | 001 | BEQ | BLT | BLE | BNE | JAL |  |  | 
LD | 010 | LB | LH | LW | LD | LBU | LHU | LWU | 
ST | 011 | SB | SH | SW | SD |  |  |  | 
ALU | 100 | ADDI |  |  |  | ANDI | ORI | XORI | 
ALU | 101 |  |  |  |  |  |  |  | 
 | 110 |  |  |  |  |  |  |  | 
 | 111 |  |  |  |  |  |  |  | 
Lower 3 bits
Upper 3 bits

## Slide 24: Secondary Opcode Chart
ADD, AND, OR, XOR are in the same place as ADDI etc.
Same decoding for ALU control just use OP2 instead of OP1
 | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
00000 |  |  |  |  |  |  |  | 
00001 | EQ | LT | LE | NE |  |  |  | 
00010 |  |  |  |  |  |  |  | 
00011 |  |  |  |  |  |  |  | 
00100 | ADD |  |  |  | AND | OR | XOR | 
00101 | SUB |  |  |  | NAND | NOR | NXOR | 
00110 |  |  |  |  |  |  |  | 
00111 |  |  |  |  |  |  |  | 
More significant 5 bits
Less significant 3 bits

## Slide 25: Secondary Opcode Chart
Comparison instructions
  LT Rd, Rs, Rt => if (Rs < Rt) the Rd =1 else Rd = 0
 | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
00000 |  |  |  |  |  |  |  | 
00001 | EQ | LT | LE | NE |  |  |  | 
00010 |  |  |  |  |  |  |  | 
00011 |  |  |  |  |  |  |  | 
00100 | ADD |  |  |  | AND | OR | XOR | 
00101 | SUB |  |  |  | NAND | NOR | NXOR | 
00110 | RSHF | LSHF |  |  |  |  |  | 
00111 |  |  |  |  |  |  |  | 
More significant 5 bits
Less significant 3 bits

## Slide 26: Instruction Format
{OP1, OP2, rd, rs, rt} (In assembly, opcode, Rd, Rs, Rt}
  This format is used when OP1 is EXT
  rd = rs OP2 rt
  rd = (rs OP2 rt)? 1 : 0 when OP2 is EQ, LT, LE, NE
{OP1, rs, rt, imm} (In assembly, opcode, rs, rt, imm or SW/LW, rt, imm(rs))
  This format is used for everything else
  SW: mem[rs+ sxt(imm)] = rt
  LW: rt = mem[rs + sxt(imm)]
  B*: if (rs OP1 rt) PC = PC + 4 + (sxt(imm)*4) (BEQ, BLT, BLE, BNE)
  ALUI: rt = rs OP1 sxt (imm) (ADDI, ANDI, ORI, XORI)
  JAL: rt <= PC+4, PC <= rs + 4*sxt(imm);
    Question: what should JAL R1, 0(R1) do?

## Slide 27: Assembler syntax
.ORG <number>
  Changes “current” address to <number>
.WORD <value>
  Places 32-bit word <value> at the current address
  <value> can be a number or a label name
  If label name, value is the full 32-bit label_addr
.NAME <name>=<value>
  Defines a name (label) with a given value (number)
  Otherwise we would have to name constants using
  .ORG 1 One:

## Slide 28: RSHF, LSHF
LSHF (Left shift and insert zeros for lower bits)
  rd = rs << (rt)
RSHF (Arithmetic right shift. Right shift and then sign extensions)
  rd = SEXT(rs >> (rt) )

## Slide 29: Register Names
Each register has multiple names
    R0 is reserved for zero
    R1..R4 are also A0..A3 (function arguments, caller saved)
    R4 is also RV (return value, caller saved)
    R5..R6 are also T0..T1 (temporaries, caller saved)
    R7..R9 are also S0..S2 (callee-saved values)
    R10 reserved for assembler use
    R11..R12 reserved for system use (we’ll see later for what)
    R13 is FP (frame pointer)
    R14 is SP (stack pointer)
    R15 is RA (return address)
  Stack grows down, SP points to lowest in-use address

## Slide 30: Pseudo-instructions
Do not actually exist in the ISA
  Translate into existing instructions
  Can use R10 (see below)
    That’s why we reserved it for assembler use
We will have (for now)
NOT Ri,Rj => NAND Ri,Rj,Rj
CALL Imm(Ri) => JAL RA, Imm(Ri)
RET => JAL R10, 0(RA)
JMP Imm(Ri) => JAL R10,Imm(Ri)

## Slide 31: More pseudo-instructions
BGT Ry, Rx, Label => BLT Rx, Ry, Label
BGE Ry, Rx, Label => BLE Rx, Ry, Label
BR Label => BEQ, Zero, Zero, Label
GT Rz, Ry, Rx => LT Rz, Rx, Ry
GE Rz, Ry, Rx => LE Rz, Rx, Ry
SUBI Ry, Rx, Imm => ADDI Ry, Rx – Imm

## Slide 32: Memory?
Separate inst and data memory?
  Good: Our design will be faster, cheaper
  Bad: How does one load programs into memory?
We’ll have separate imem and dmem for now
  We’ll see later how to unify them
How much memory?
  There are 239,616 memory bits on-chip, so
  8kB (2048 32-bit words) of imem
  8kB (2048 32-bit words) of dmem
  Leaves about half of memory bits on the FPGA chip (for register file, debugging in SignalTap, etc.)

## Slide 33: Input/Output?
We want our programs to
  Read SW, KEY (so we can interact with it)
  Write to HEX, LEDR
  Maybe some more I/O
Need instructions for this!
  Special instruction for each device, e.g. “WRLEDR”
    Extensions are hard (change processor as each device added)
  Special IN/OUT instructions
    Assign “addresses” to devices, then use IN/OUT to read/write
  Memory-mapped I/O (this is what we’ll use)
    Each device gets a memory address, LW/SW can be used for I/O
    Can’t use those memory locations as normal memory!

## Slide 34: Memory mapped IO
 |  | Bits | Addr | Value
Input | KEY | 4 bits | 0xFFFFF080 | 0 ~ F : {28’b0, ~KEY} 0: no key,
 | SW | 10 bits | 0xFFFFF090 | 0 ~ 2^10-1: {22’d0, SWd}
output | LEDR | 10 bits | 0xFFFFF020 | Display value [9:0]
 | HEX | 4*6 = 24 bits | 0xFFFFF000 | Display value [23:0]
I/O accesses are done with Load/Store instructions
SWd: debounced value of SW